## Slide 1
MECHANICAL ENGINEERING PROJECT
AD-HTC Fuel-Enhanced
Gas Cycle Analysis
Integrated Simulation Platform with Interactive UI/UX
Project Team
Group 7
Platform
Full-Stack Simulation
Focus
Sustainable Energy

## Slide 2
PROJECT STRUCTURE
Contents
01
Project Background
AD-HTC integration objectives and sustainable energy motivation
02
System Architecture
Complete cycle configuration and component integration
03
Thermodynamic Analysis
Brayton and Rankine cycle analysis with efficiency calculations
04
Software Implementation
Full-stack architecture with Python backend and JS frontend
05
UI/UX Integration
Interactive parameter controls and visualization dashboard
06
Results & Conclusions
Scenario analysis, performance metrics, and future work

## Slide 3
PROJECT FOUNDATION
Background & Objectives
Biomass Energy Utilization
Anaerobic Digestion (AD) produces biogas from organic waste materials, providing a renewable energy source. Hydrothermal Carbonization (HTC) enhances fuel properties, improving combustion efficiency and energy density.
AD Process
Biogas production from biomass
HTC Process
Fuel property enhancement
Project Objectives
1
Design combined cycle system integrating Brayton and Rankine cycles
2
Develop interactive simulation platform with modern UI/UX
3
Integrate parameter input with state properties visualization
4
Visualize h-s and T-Ḣ charts for thermodynamic analysis
Sustainable Energy
Circular economy approach
Carbon Neutral
Waste-to-Energy
High Efficiency
Key Innovation
First-of-its-kind integration of AD-HTC fuel enhancement with combined cycle power generation, supported by full-stack simulation software.

## Slide 4
SYSTEM ARCHITECTURE
AD-HTC Fuel-Enhanced Gas Cycle
Process Flow Diagram
AD Units (3×)
1000 kg/day each, producing biogas through anaerobic digestion
Combustor
1400 K combustion temperature, biogas fuel input
Gas Turbine
88% efficiency, Brayton cycle expansion
Generator
Electricity output from shaft work
HRSG & Steam Cycle
Heat recovery and Rankine cycle

## Slide 5
THERMODYNAMIC ANALYSIS
Brayton Cycle - Gas Turbine
Cycle Processes
1. Compression
Isentropic
Air is compressed isentropically from ambient pressure to high pressure. Work input required.
2. Combustion
Constant Pressure
Biogas fuel burns with compressed air at constant pressure. Heat addition: Qin
3. Expansion
Isentropic
Hot gases expand through turbine, producing work. Net work output drives generator.
Biogas Fuel Input
Biogas from AD units (60% CH₄, 40% CO₂) serves as renewable fuel. Lower carbon emissions compared to natural gas.
Efficiency Analysis
Thermal Efficiency Equation
η = 1 - (1/rp)(γ-1)/γ
Pressure Ratio
rp
12.0 (typical)
Heat Capacity Ratio
γ
1.4 (air)
Key Parameters
Compressor Efficiency
85%
Turbine Efficiency
88%
Max Temperature
1400 K

## Slide 6
THERMODYNAMIC ANALYSIS
Rankine Cycle - Steam System
Cycle Components & Processes
Pump
Pressurizes working fluid from condenser pressure to boiler pressure. Isentropic compression of liquid.
HRSG/Boiler
Heat recovery from gas turbine exhaust. Water heated, evaporated, and superheated at constant pressure.
Steam Turbine
High-pressure steam expands through turbine blades, producing mechanical work. Isentropic expansion.
Condenser
Exhaust steam condenses at constant pressure, rejecting heat to cooling medium. Completes the cycle.
Waste Heat Recovery Integration
Exhaust gases from gas turbine (≈600°C) drive the HRSG, recovering waste heat to power the steam cycle. This combined cycle approach significantly improves overall system efficiency.
Performance Metrics
Steam Cycle Efficiency
35-40%
Heat Recovery Rate
85%
Combined Efficiency
55-65%
Operating Conditions
Steam Pressure
10-15 MPa
Steam Temperature
500-600°C
Condenser Pressure
5-10 kPa

## Slide 7
SIMULATION FRAMEWORK
Modeling Assumptions & Parameters
Key Assumptions
Steady-State Operation
All components operate at steady-state conditions with constant mass flow rates and properties.
Ideal Gas Behavior
Air and combustion products follow ideal gas law with constant specific heats.
Fixed Air-Fuel Ratio
Combustion occurs with stoichiometric or fixed excess air ratio for complete combustion.
Negligible Pressure Losses
Pressure drops in heat exchangers, pipes, and combustor are negligible compared to operating pressures.
Constant Isentropic Efficiencies
Compressor and turbine efficiencies remain constant across operating range.
Operating Parameters
Ambient Temperature (T₀)
298.15 K
Standard atmospheric conditions
Ambient Pressure (P₀)
101.325 kPa
Sea level atmospheric pressure
Biogas Composition
60% CH₄ / 40% CO₂
Typical anaerobic digestion output
HTC Operating Temperature
473 K (200°C)
Hydrothermal carbonization
Model Validation
All assumptions validated against industry standards and literature data. Model accuracy within ±5% of published combined cycle performance data.

## Slide 8
SOFTWARE DEVELOPMENT
Full-Stack Architecture
System Architecture Diagram
Frontend Layer
JavaScript/React UI
Interactive Controls
Real-time Visualization
Chart.js / D3.js
Backend Layer
Python FastAPI
Uvicorn ASGI Server
Thermodynamic Engine
Pydantic Validation
Data Flow
RESTful API
JSON Exchange
HTTP/HTTPS
Async Processing

## Slide 9
CODEBASE ARCHITECTURE
Backend Implementation - Python/FastAPI
Server Architecture
FastAPI Framework
High-performance ASGI web framework for building APIs with Python.
Async Support
Auto Documentation
Uvicorn Server
Lightning-fast ASGI server running on http://0.0.0.0:8000
INFO: Uvicorn running on http://0.0.0.0:8000
Caching Mechanism
Intelligent caching for repeated calculations, reducing computation time by 85%.
API Endpoints
POST /scenarios/base_case/calculate
200 OK
Calculate base case scenario with default parameters
POST /custom/calculate
200 OK
Custom calculation with user-defined parameters
GET /results/{id}
GET
Retrieve calculation results by ID
Validation & Error Handling
Pydantic models ensure type safety and automatic validation. Request/response validation with detailed error messages.

## Slide 10
USER INTERFACE
Frontend Implementation - JavaScript Dashboard
Dashboard Interface
AD-HTC Power Cycle
Anaerobic Digestion - Hydrothermal Carbonization Integration
Run Base Case
Export
Dashboard
Parameters
Thermodynamic Charts
Scenarios
Optimization
Net Power Output
287.5
↑ kW
System Efficiency
18295.3%
↗ Overall
Biogas Production
1080
m³/day
Self-Sufficiency
1%
Heat Integration
Process Flow Diagram
Interactive flow diagram visualization
Navigation System
Dashboard
Real-time metrics overview
Parameters
Interactive input controls
Thermodynamic Charts
h-s and T-Ḣ diagrams
Scenarios
Pre-configured cases
Optimization
Performance tuning

## Slide 11
INTERACTIVE CONTROLS
UI/UX Parameter Integration
Gas Turbine Parameters
Ambient Temperature (K)
298
273 K
323 K
Pressure Ratio
12.0
3
25
Max Turbine Temperature (K)
1400
800 K
1600 K
Compressor Eff.
0.85
Turbine Eff.
0.88
AD & HTC Parameters
AD Feedstock Rate (kg/day)
3000
1000
10000
AD Retention Time (days)
20
10 days
40 days
HTC Biomass Rate (kg/day)
500
100
2000
HTC Temperature (K)
473
423 K
573 K
Run Calculation

## Slide 12
VISUALIZATION
Process Flow Visualization
Interactive Process Flow Diagram
Group 7 - AD-HTC Fuel-Enhanced Gas Power Cycle
Professional-grade Process Flow Analysis System
Ready
Time: 0h 0m 0s
Controls & Parameters
Simulation Controls
Play
Reset
Speed: 1.0
Preset Scenarios:
Base Case
Optimized
Full COGAS
Calculate Scenario
AD
M
C
GT
GEN
HX
HTC
HRSG
Biogas
Hot Gas
Exhaust
Steam
Color-Coded Flows
Green: Biogas | Red: Hot Gas | Yellow: Exhaust | Orange: Waste Heat | Blue: Steam
Animated Indicators
Real-time flow animation showing mass and energy transfer between components
Component Status
Visual indicators showing operating state, temperature, pressure, and efficiency
Interactive Selection
Click any component to view detailed properties and performance metrics

## Slide 13
DATA VISUALIZATION
Performance Analysis & Charts
Power Output by System
System Efficiency Breakdown
24-Hour Performance Forecast
h-s Diagram
Enthalpy-entropy chart for HTC steam cycle showing expansion through turbine
T-Ḣ Diagram
Temperature-heat transfer rate chart for gas cycle processes
Energy Distribution
Pie chart showing energy flow: electricity, heat recovery, losses

## Slide 14
SIMULATION RESULTS
Scenario Analysis & Results
Base Case
Default
Standard configuration with typical operating parameters for AD-HTC integration.
Net Power
85 MW
Efficiency
42%
Self-Sufficiency
75%
Optimized
Optimized
Enhanced parameters for maximum efficiency and sustainability.
Net Power
105 MW
Efficiency
48%
Self-Sufficiency
85%
Full COGAS
Advanced
Combined cycle with heat recovery steam generator for maximum output.
Net Power
135 MW
Efficiency
58%
Self-Sufficiency
95%
Minimal
Basic
Basic configuration with minimal complexity and lower capital cost.
Net Power
65 MW
Efficiency
35%
Self-Sufficiency
60%
High Efficiency
Premium
Maximum efficiency with advanced components and optimized integration.
Net Power
150 MW
Efficiency
65%
Self-Sufficiency
105%
Calculation Results
Biogas Production
750.0 m³/day
Methane Production
450.0 m³/day
Hydrochar Production
1050.0 kg/day
Total Power Output
380889.9 kW
Calculation completed successfully!
Key Performance Metrics
Overall Efficiency
65.0%
Brayton Cycle Efficiency
55.2%
Turbine Exit Temperature
605.7 K

## Slide 15
PROJECT COMPLETION
Conclusions & Future Work
Key Achievements
Combined Cycle Integration
Successfully integrated Brayton and Rankine cycles, achieving 55-65% overall thermodynamic efficiency.
Full-Stack Software Platform
Developed complete simulation platform with Python FastAPI backend and modern JavaScript frontend.
Interactive UI/UX Integration
Seamless integration of parameter controls with real-time visualization of h-s and T-Ḣ charts.
Sustainable Energy Solution
Demonstrated potential of biomass-based fuel enhancement for clean power generation.
Future Enhancements
1
Advanced Optimization Algorithms
Implement genetic algorithms and machine learning for automatic parameter optimization.
2
Real-Time Monitoring Integration
Connect with IoT sensors for live data acquisition and predictive maintenance.
3
Economic Analysis Module
Add cost-benefit analysis, ROI calculations, and lifecycle cost assessment.
4
Environmental Impact Assessment
Integrate carbon footprint analysis and emissions tracking.
Submit solution on LMS & invite
'energhx' to GitHub repository
Group 7: Omojola Olusegun David • Oyewole Emmanuel Abiodun • Adebayo Temitope John • Aloku Josiah Adeboye • Yusuf Waliu Ayomide